## Slide 1
KL DEEMED TO BE UNIVERSITY • DEPARTMENT OF ECE
SAMYAK 2026
LOGIC MATRIX
THINK / ANALYZE / SOLVE
Official Competitive Question Paper — 2nd Year BTech Technical Fest
DATE: 29-10-2026 | TIME: 9:30 AM – 12:30 PM (3 Hours) | VENUE: R406A | TOTAL MARKS: 80
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 1 of 27
Notes: PROCTORING GUIDELINES:
- Welcome all participant teams (2nd-year BTech ECE/EEE/CSE students).
- Verify registration badges against the portal list.
- Ensure mobile phones, smartwatches, and programmable calculators are deposited at the proctor desk.
- Event Duration: 180 Minutes (9:30 AM to 12:30 PM). Total Marks: 80.

## Slide 2
KL ECE | SAMYAK 2026 | LOGIC MATRIX
Rules, Structure & Marking Scheme
[SECTIONS] EXAMINATION STRUCTURE
• Section A: MCQs (Q1 – Q10)
10 Questions @ 2 Marks = 20 Marks • Time Cue: ~30 mins total • Marking: +2 for correct, -0.5 for wrong
• Section B: Design Problems (Q11 – Q18)
8 Questions @ 5 Marks = 40 Marks • Time Cue: ~90 mins total • Stepwise evaluation for truth tables & K-maps
• Section C: Logic Puzzles (Q19 – Q20)
2 Questions @ 10 Marks = 20 Marks • Time Cue: ~40 mins total • High-level analytical & fault diagnostic puzzles
[RULES] COMPETITION CONDUCT
1. Allowed Materials: Non-programmable scientific calculators (FX-82/991 series), blue/black ballpoint pens, geometric drawing tools.
2. Answer Sheet Integrity: All final boolean expressions must be simplified to minimal SOP/POS forms unless specified otherwise.
3. K-Map Grouping Visuals: K-map cell values and loop groupings (quads, octets, pairs) MUST be explicitly drawn in answer scripts.
4. Negative Marking: Applies strictly to Section A MCQs (-0.5 marks per incorrect response; 0 for unattempted).
5. Tie-Breaker Round: Triggered automatically if top team scores are identical at 12:30 PM.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 2 of 27
Notes: PROCTORING GUIDELINES:
- Read out loud the negative marking rule (-0.5 for MCQs).
- Clarify that non-programmable calculators are allowed for propagation delay calculations.
- Distribute standardized 12-page answer booklets at 9:25 AM. Timing starts promptly at 9:30 AM.

## Slide 3
KL ECE | SAMYAK 2026 | LOGIC MATRIX
Section A: Multiple Choice Questions (Q1 – Q10)
SECTION A: MULTIPLE CHOICE QUESTIONS
• Total Questions: 10 | Marks per Question: 2 Marks | Total Section Marks: 20
• Negative Marking: -0.5 Marks for wrong answers. 0 Marks for unattempted questions.
• Topics Covered: Boolean Duality, K-Map Implicants, Universal Gate Realizations, MUX Expressions, Timing & Propagation Delay, Don't Care Optimization, Active-LOW Decoders, 6-Variable K-Map Properties, Cascade Magnitude Comparators, Self-Dual Functions.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 3 of 27
Notes: PROCTORING NOTES:
- Announce Section A start. Advise students to spend ~3 minutes per MCQ.
- Emphasize marking the final option clearly on the optical mark / answer grid.

## Slide 4
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 1: Boolean Duality Principle
[Q] QUESTION 1 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q1. Determine the Dual expression of the Boolean function: F(A, B, C) = A + A'B*C + A(B + C') Recall: The dual of a Boolean expression is obtained by swapping AND (.) and OR (+) operators, and swapping 0 and 1, without changing literal complementation.
(A) F_dual = A * (A' + B + C) * (A + B * C')
(B) F_dual = A' * (A + B' + C') * (A' + B' * C)
(C) F_dual = A * (A' + B + C) * (A * B + C')
(D) F_dual = A + (A' * B + C) + A(B' * C)
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 4 of 27
Notes: PROCTORING CUE:
- Topic: Fundamental Axioms of Boolean Algebra.
- Ensure students do NOT complement variables when forming the Dual (dual ≠ complement).

## Slide 5
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 2: Essential Prime Implicants in 4-Variable K-Map
[Q] QUESTION 2 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q2. For the 4-variable Boolean function f(A,B,C,D) = Σ m(0, 2, 5, 7, 8, 10, 13, 15), how many Essential Prime Implicants (EPIs) exist in the minimized K-map representation?
(A) 1 EPI
(B) 2 EPIs
(C) 3 EPIs
(D) 4 EPIs
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 5 of 27
Notes: PROCTORING CUE:
- Topic: K-Map Optimization & Implicant Classification.
- Remind students to plot all 8 minterms on a 4x4 grid and identify minterms covered by exactly one PI.

## Slide 6
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 3: Universal Gate Minimization
[Q] QUESTION 3 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q3. What is the absolute minimum number of 2-input NAND gates required to implement a 2-input Exclusive-OR (XOR) logic gate?
(A) 3 NAND gates
(B) 4 NAND gates
(C) 5 NAND gates
(D) 6 NAND gates
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 6 of 27
Notes: PROCTORING CUE:
- Topic: Universal Gate Logic Realization.
- Standard textbook question. Direct students to consider the shared intermediate product term (A*B)'.

## Slide 7
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 4: Multiplexer Logic Function Realization
[Q] QUESTION 4 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q4. An 8:1 Multiplexer has select inputs (S2, S1, S0) connected to variables (A, B, C). Data inputs are set as: I0=D, I1=D', I2=0, I3=1, I4=D, I5=D, I6=1, I7=0. Which minterm expression F(A,B,C,D) does this MUX realize?
(A) F = Σ m(0, 3, 4, 8, 9, 10, 13, 14)
(B) F = Σ m(0, 3, 7, 8, 9, 10, 12, 13)
(C) F = Σ m(0, 3, 6, 8, 9, 10, 12, 14)
(D) F = Σ m(1, 3, 6, 8, 9, 11, 12, 14)
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 7 of 27
Notes: PROCTORING CUE:
- Topic: Combinational Logic via Multiplexers.
- Students should map S2=A, S1=B, S0=C and evaluate I_k for D=0 and D=1.

## Slide 8
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 5: Propagation Delay & Critical Path Analysis
[Q] QUESTION 5 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q5. A 4-bit Ripple Carry Adder is constructed using Full Adders, where each Full Adder consists of 2-input XOR gates (delay t_XOR = 5 ns), 2-input AND gates (delay t_AND = 2 ns), and 2-input OR gates (delay t_OR = 2 ns). What is the total critical path propagation delay for the worst-case carry propagation?
(A) 18 ns
(B) 21 ns
(C) 24 ns
(D) 29 ns
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 8 of 27
Notes: PROCTORING CUE:
- Topic: Gate Delays & Timing in Combinational Adders.
- Formula: t_ripple = t_XOR + (N-1)*t_carry_stage + t_sum_stage.

## Slide 9
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 6: Incompletely Specified Functions & Don't Cares
[Q] QUESTION 6 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q6. Given the incomplete Boolean function f(A,B,C,D) = Σ m(1, 3, 7, 11, 15) with don't care conditions d(A,B,C,D) = Σ d(0, 2, 5), what is the minimal Sum-of-Products (SOP) expression?
(A) F = C'D + A'B
(B) F = CD + A'B'
(C) F = CD + A'D
(D) F = C'D' + AD
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 9 of 27
Notes: PROCTORING CUE:
- Topic: Don't Care Optimization in K-Maps.
- Check if students include optional don't cares d(0,2) to form an octet or quad.

## Slide 10
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 7: Active-LOW Decoder Logic Implementation
[Q] QUESTION 7 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q7. A 3-to-8 line decoder with Active-LOW outputs (Y0' through Y7') is used to implement a logic function F(A,B,C). If the desired output is F = Σ m(1, 3, 6, 7), which external gate must be connected to the decoder outputs?
(A) A 4-input AND gate connected to Y1', Y3', Y6', Y7'
(B) A 4-input NAND gate connected to Y1', Y3', Y6', Y7'
(C) A 4-input OR gate connected to Y1', Y3', Y6', Y7'
(D) A 4-input NOR gate connected to Y1', Y3', Y6', Y7'
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 10 of 27
Notes: PROCTORING CUE:
- Topic: Decoder-based Logic Design.
- Active-LOW outputs mean selected minterms produce 0. Applying DeMorgan: (Y1' * Y3' * Y6' * Y7')' = Y1 + Y3 + Y6 + Y7.

## Slide 11
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 8: 6-Variable K-Map Sub-cube Adjacency
[Q] QUESTION 8 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q8. In a 6-variable K-map consisting of four 4-variable sub-maps (M00, M01, M10, M11 corresponding to variables U,V), which cell in sub-map M11 is logically adjacent to cell m(12) located in sub-map M00?
(A) m(28)
(B) m(44)
(C) m(60)
(D) No cell in M11 is adjacent to m(12)
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 11 of 27
Notes: PROCTORING CUE:
- Topic: High-Dimensional K-Map Geometry.
- Cell 12 in M00 is UVWX'Y'Z = 001100. Cell in M11 with same WXYZ is 111100 = 60. Hamming distance must be checked.

## Slide 12
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 9: Cascaded 4-bit Magnitude Comparators
[Q] QUESTION 9 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q9. Two 4-bit magnitude comparators (IC 7485) are cascaded to compare two 8-bit numbers A = A7..A0 and B = B7..B0. If the lower stage inputs receive A4..A1 and upper stage receives A7..A4, which cascading input pins of the most significant stage must be tied to logic HIGH?
(A) A < B cascade input
(B) A = B cascade input
(C) A > B cascade input
(D) Both A < B and A > B inputs
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 12 of 27
Notes: PROCTORING CUE:
- Topic: Magnitude Comparator Cascading Architecture.
- IC 7485 requires A=B_in = 1 at the least significant stage for proper tie resolution.

## Slide 13
SECTION A — MULTIPLE CHOICE QUESTIONS
Question 10: Self-Dual Boolean Functions
[Q] QUESTION 10 OF 20 | [TIME] 3 Mins | [WEIGHT] 2 Marks | [PENALTY] -0.5 MARKS
Q10. A Boolean function F(x1, x2, x3) is self-dual if F(x1, x2, x3) = F'(x1', x2', x3'). How many distinct self-dual Boolean functions of n = 3 variables exist?
(A) 8 functions
(B) 16 functions
(C) 32 functions
(D) 256 functions
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 13 of 27
Notes: PROCTORING CUE:
- Topic: Advanced Boolean Symmetry & Self-Duality.
- Formula for self-dual functions of n variables: 2^(2^(n-1)). For n=3, 2^(2^2) = 2^4 = 16.

## Slide 14
KL ECE | SAMYAK 2026 | LOGIC MATRIX
Section B: Short Answer & Design Problems (Q11 – Q18)
SECTION B: SHORT ANSWER & DESIGN PROBLEMS
• Total Questions: 8 | Marks per Question: 5 Marks | Total Section Marks: 40
• Evaluation: Stepwise credit for Truth Tables, Algebraic Axioms, K-Map Visual Groups, and Circuit Diagrams.
• Topics Covered: 1. Algebraic Reduction & Universal Gate Conversion 2. 4-Variable K-Map Prime Implicant Analysis 3. 6-Variable K-Map Sub-map Minimization 4. Multiplexer Tree Logic Realization 5. Static Hazard Elimination & Timing Diagrams 6. Full Subtractor via NOR-NOR Logic 7. Priority Encoder & Valid Bit Circuitry 8. Odd Parity Generator & Propagation Delay
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 14 of 27
Notes: PROCTORING CUE:
- Announce Section B start. Remind students to write step-by-step logic derivations.
- Emphasize that final logic circuits must use standard IEEE gate symbols.

## Slide 15
SECTION B — SHORT ANSWER & DESIGN PROBLEMS
Question 11: Algebraic Simplification & NAND Realization
[Q] QUESTION 11 OF 20 | [TIME] 10 Mins | [MAX MARKS] 5 Marks
Q11. Simplify the given Boolean expression algebraically using Boolean theorems: F(A, B, C) = A'B'C' + A'B'C + A'BC' + AB'C' After finding the minimal Sum-of-Products (SOP) expression, convert the function into an equivalent 2-level NAND-NAND circuit.
[TASKS] REQUIRED STEPS & SUB-TASKS FOR FULL MARKS:
• (a) Show step-by-step algebraic manipulation citing Boolean laws (Adjacency, Absorption, DeMorgan) [2 Marks]
• (b) State the minimal SOP expression [1 Mark]
• (c) Draw the equivalent logic diagram using 2-input NAND gates ONLY [2 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 15 of 27
Notes: EVALUATION GUIDELINES:
- Check step 1: A'B'(C'+C) + A'BC' + AB'C' = A'B' + A'BC' + AB'C'.
- Check step 2: A'B' + A'BC' = A'(B' + BC') = A'(B' + C').
- Final Minimal SOP: F = A'B' + A'C' + B'C' or F = (AB + AC + BC)'.
- NAND diagram must show inverted inputs generated via NAND ties.

## Slide 16
SECTION B — SHORT ANSWER & DESIGN PROBLEMS
Question 12: 4-Variable K-Map & Implicant Classification
[Q] QUESTION 12 OF 20 | [TIME] 12 Mins | [MAX MARKS] 5 Marks
Q12. A 4-variable Boolean function is defined as: F(W, X, Y, Z) = Σ m(0, 1, 2, 8, 9, 10, 11, 14, 15) + d(3, 7) Perform a rigorous K-map minimization on a 4x4 grid.
[TASKS] REQUIRED STEPS & SUB-TASKS FOR FULL MARKS:
• (a) Draw the complete 4x4 K-map grid with correct Gray code indexing (00, 01, 11, 10) [1 Mark]
• (b) Circle and identify ALL Prime Implicants (PIs) and highlight Essential Prime Implicants (EPIs) [2 Marks]
• (c) Write the minimal SOP expression and verify whether any alternative minimal expressions exist [2 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 16 of 27
Notes: EVALUATION GUIDELINES:
- Grid must be labeled WX (rows) and YZ (cols).
- Don't care d(3) completes Octet m(0,1,2,3,8,9,10,11) -> W' + W? Actually W=0/1 gives W'Z'... Let's evaluate carefully in solution deck.
- Essential PIs must be clearly indicated with distinct loop colors.

## Slide 17
SECTION B — SHORT ANSWER & DESIGN PROBLEMS
Question 13: 6-Variable K-Map Minimization Across Sub-maps
[Q] QUESTION 13 OF 20 | [TIME] 15 Mins | [MAX MARKS] 5 Marks
Q13. Minimize the following 6-variable function F(A, B, C, D, E, F): F = Σ m(0, 4, 16, 20, 32, 36, 48, 52) + d(1, 5, 17, 21) where variables A,B select one of four 4-variable sub-maps (M00, M01, M10, M11) and C,D,E,F index cells within each sub-map.
[TASKS] REQUIRED STEPS & SUB-TASKS FOR FULL MARKS:
• (a) Plot minterms across all four 4x4 sub-maps for (A,B) = (00, 01, 10, 11) [2 Marks]
• (b) Identify 3D / 4D sub-cube adjacencies across sub-maps [1.5 Marks]
• (c) Derive the overall minimal SOP expression [1.5 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 17 of 27
Notes: EVALUATION GUIDELINES:
- Minterms are 0, 4, 16, 20, 32, 36, 48, 52.
- Binary: 000000, 000100, 010000, 010100, 100000, 100100, 110000, 110100.
- Note that in ALL sub-maps, C,D,E,F = 0000 and 0100! Thus A and B are independent! Excellent reduction!

## Slide 18
SECTION B — SHORT ANSWER & DESIGN PROBLEMS
Question 14: Multiplexer Tree Design (4:1 MUX Logic Realization)
[Q] QUESTION 14 OF 20 | [TIME] 12 Mins | [MAX MARKS] 5 Marks
Q14. Implement the 4-variable logic function: F(A, B, C, D) = Σ m(0, 1, 3, 4, 8, 9, 15) using a single 4:1 Multiplexer and minimal external logic gates. Connect variables A and B to the MUX select lines S1 and S0 respectively.
[TASKS] REQUIRED STEPS & SUB-TASKS FOR FULL MARKS:
• (a) Construct the MUX implementation table derived from inputs C and D for each combination of AB = (00, 01, 10, 11) [2 Marks]
• (b) Determine the input expressions for I0, I1, I2, I3 in terms of C and D [1.5 Marks]
• (c) Draw the complete circuit diagram showing the 4:1 MUX, select line connections, and input gate logic [1.5 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 18 of 27
Notes: EVALUATION GUIDELINES:
- AB=00: m(0,1,3) -> C'D' + C'D + CD = C' + CD = C' + D.
- AB=01: m(4) -> C'D'.
- AB=10: m(8,9) -> C'D' + C'D = C'.
- AB=11: m(15) -> CD.

## Slide 19
SECTION B — SHORT ANSWER & DESIGN PROBLEMS
Question 15: Static Hazard Detection & Elimination
[Q] QUESTION 15 OF 20 | [TIME] 12 Mins | [MAX MARKS] 5 Marks
Q15. Consider the combinational circuit implementing F = A*B + A'*C. When inputs are B=1 and C=1, a transition of input A from 1 to 0 produces a transient glitch (Static 1-Hazard) due to inverter delay.
[TASKS] REQUIRED STEPS & SUB-TASKS FOR FULL MARKS:
• (a) Draw the timing diagram showing propagation delay of inverter A' causing both product terms to briefly equal 0 [2 Marks]
• (b) Apply the Consensus Theorem to identify the essential hazard-free cover term [1.5 Marks]
• (c) Draw the hazard-free modified circuit diagram [1.5 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 19 of 27
Notes: EVALUATION GUIDELINES:
- Timing diagram must explicitly highlight the delta-t window where A=0 and A'=0 due to gate propagation delay.
- Consensus term between AB and A'C is BC.
- Hazard-free function: F = AB + A'C + BC.

## Slide 20
SECTION B — SHORT ANSWER & DESIGN PROBLEMS
Question 16: Full Subtractor Design using NOR-NOR Logic
[Q] QUESTION 16 OF 20 | [TIME] 12 Mins | [MAX MARKS] 5 Marks
Q16. Design a 1-bit Full Subtractor that computes Difference (Diff) and Borrow-out (B_out) for inputs A (Minuend), B (Subtrahend), and B_in (Borrow-in).
[TASKS] REQUIRED STEPS & SUB-TASKS FOR FULL MARKS:
• (a) Construct the complete 8-row Truth Table for Diff and B_out [1 Mark]
• (b) Derive canonical Product-of-Sums (POS) expressions and simplify using K-maps [2 Marks]
• (c) Draw the complete logic implementation using 2-input NOR gates ONLY [2 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 20 of 27
Notes: EVALUATION GUIDELINES:
- Diff = A ⊕ B ⊕ B_in.
- B_out = A'B + A'B_in + B B_in = (A + B')' + (A + B_in')' + (B' + B_in')' in NOR logic.
- Verify all NOR gate transformations.

## Slide 21
SECTION B — SHORT ANSWER & DESIGN PROBLEMS
Question 17: 4-to-2 Priority Encoder with Valid Output
[Q] QUESTION 17 OF 20 | [TIME] 10 Mins | [MAX MARKS] 5 Marks
Q17. Design a 4-to-2 Priority Encoder with Active-HIGH inputs D3, D2, D1, D0, where D3 has the highest priority and D0 has the lowest priority. The encoder outputs are Y1, Y0, and a Valid bit V.
[TASKS] REQUIRED STEPS & SUB-TASKS FOR FULL MARKS:
• (a) Write the truth table specifying input conditions and don't care states (X) [1.5 Marks]
• (b) Derive minimal Boolean expressions for Y1, Y0, and V using K-maps [1.5 Marks]
• (c) Draw the gate-level schematic diagram [2 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 21 of 27
Notes: EVALUATION GUIDELINES:
- Output Y1 = D3 + D2.
- Output Y0 = D3 + D2' D1.
- Valid V = D3 + D2 + D1 + D0.

## Slide 22
SECTION B — SHORT ANSWER & DESIGN PROBLEMS
Question 18: Parity Generator / Checker & Timing Analysis
[Q] QUESTION 18 OF 20 | [TIME] 12 Mins | [MAX MARKS] 5 Marks
Q18. Design a 4-bit Odd Parity Generator (accepts data bits P3 P2 P1 P0 and outputs odd parity bit P_odd) and a corresponding 5-bit Odd Parity Checker (outputs Error bit E).
[TASKS] REQUIRED STEPS & SUB-TASKS FOR FULL MARKS:
• (a) Write the XOR/XNOR logic equations for P_odd and Error bit E [1.5 Marks]
• (b) Draw the complete logic circuit using 2-input XOR gates organized in a tree structure [2 Marks]
• (c) Calculate total propagation delay from input P3..P0 to Error bit E if each XOR gate has t_pd = 3.5 ns [1.5 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 22 of 27
Notes: EVALUATION GUIDELINES:
- Tree structure has depth log2(4) = 2 stages for generator + 1 stage for checker = 3 stages total.
- Delay = 3 * 3.5 ns = 10.5 ns.

## Slide 23
KL ECE | SAMYAK 2026 | LOGIC MATRIX
Section C: Tricky Puzzles & Brainteasers (Q19 – Q20)
SECTION C: TRICKY PUZZLES & BRAINTEASERS
• Total Questions: 2 | Marks per Question: 10 Marks | Total Section Marks: 20
• Purpose: Test high-level analytical problem solving, fault diagnosis, and structural logic optimization.
• Q19: The Black-Box Fault Diagnostic Puzzle (Stuck-At Fault Testing & Test Vector Generation) • Q20: The Self-Complementing Excess-3 Digital Lock Puzzle (Structural Gate Reduction & 9's Complement)
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 23 of 27
Notes: PROCTORING CUE:
- Announce Section C start. Remind teams that these are 10-mark complex reasoning problems.
- Allocate ~20 minutes per puzzle.

## Slide 24
SECTION C — TRICKY PUZZLES & BRAINTEASERS
Question 19: The Faulty Black-Box Diagnostic Puzzle
[PUZZLE 1 OF 2] | [TIME] 20 Mins | [MAX MARKS] 10 Marks (HIGH WEIGHTAGE)
Q19. A sealed digital module contains a 3-input majority logic function F(A,B,C) = AB + BC + CA constructed using three 2-input AND gates feeding a 3-input OR gate. During quality testing, a technician discovers that exactly ONE internal gate output node is suffering from a Stuck-at-0 (s-a-0) fault. You are permitted to apply test vectors (ABC) at the external inputs and observe the single output F.
[TARGET] PUZZLE CHALLENGE REQUIREMENTS:
• (a) Construct the Fault Table showing expected output vs actual output for all 8 input combinations (000 to 111) under each candidate node fault (Node N1: AB, Node N2: BC, Node N3: CA, Node N4: OR output) [4 Marks]
• (b) Determine the ABSOLUTE MINIMAL set of test vectors required to uniquely locate and diagnose which specific node has the stuck-at-0 fault [3 Marks]
• (c) Prove why a single test vector ABC = 111 is insufficient for fault identification [3 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 24 of 27
Notes: EVALUATION GUIDELINES:
- Fault table must evaluate F for Node 1 s-a-0, Node 2 s-a-0, Node 3 s-a-0.
- Minimal test set requires 3 vectors: 110, 011, 101.
- Complete diagnostic matrix evaluation required.

## Slide 25
SECTION C — TRICKY PUZZLES & BRAINTEASERS
Question 20: The Self-Complementing Lock & Switch Matrix Puzzle
[PUZZLE 2 OF 2] | [TIME] 20 Mins | [MAX MARKS] 10 Marks (HIGH WEIGHTAGE)
Q20. A high-security vault uses an Excess-3 BCD input code X3 X2 X1 X0 representing a decimal digit D (0 to 9). The lock requires a circuit that outputs Y3 Y2 Y1 Y0 representing the 9's complement of D (i.e., 9 - D in Excess-3 BCD). A naive engineer proposes building 4 separate K-maps for Y3, Y2, Y1, Y0 using all 16 minterm slots (including 6 don't care conditions for invalid BCD inputs 0,1,2,13,14,15).
[TARGET] PUZZLE CHALLENGE REQUIREMENTS:
• (a) Prove mathematically using the Self-Complementing Property of Excess-3 code that 9's complement is obtained by simply bitwise complementing inputs! [3 Marks]
• (b) Derive the minimal Boolean expressions for Y3, Y2, Y1, Y0 under both the naive K-map approach and the self-complementing bit-inversion approach [4 Marks]
• (c) Show that the self-complementing property reduces total gate count from 14 gates to 4 INVERTER gates (71.4% gate reduction!) [3 Marks]
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 25 of 27
Notes: EVALUATION GUIDELINES:
- Excess-3 representation of D: D + 3. Excess-3 representation of 9-D: (9-D)+3 = 12-D = 15 - (D+3) = Bitwise NOT of (D+3)!
- Proof is elegant and highlights fundamental digital design theory.

## Slide 26
KL ECE | SAMYAK 2026 | LOGIC MATRIX
Sudden Death Tie-Breaker Round (In Case of Equal Scores)
[TIE-BREAKER] SUDDEN DEATH QUESTIONS
In the event of a tie in overall score at 12:30 PM, the tied teams will face the following 3 rapid-fire questions (2 minutes per question):
• TB Q1 (Hazard Elimination Speed Test):
Identify the consensus term required to eliminate the static 0-hazard in the POS function F = (A + B)(A' + C).
• TB Q2 (Multiplexer Tree Capacity):
How many 2:1 Multiplexers are required to construct a 64:1 Multiplexer tree without any external logic gates?
• TB Q3 (Universal Gate Count Challenge):
What is the minimum number of 2-input NOR gates required to implement a 2-input XNOR gate?
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 26 of 27
Notes: PROCTORING GUIDELINES:
- Conduct tie-breaker ONLY if teams tie for 1st, 2nd, or 3rd place.
- Time limit: 2 minutes per question. First team to submit correct written answer wins.

## Slide 27
TIME IS UP!
SAMYAK 2026 — LOGIC MATRIX COMPETITION CONCLUDED
1. Please stop writing immediately and assemble your answer booklets. 2. Ensure your Team Registration ID and College Name are clearly written on Page 1. 3. Hand over your answer booklet to the proctoring desk in Room R406A. 4. Official evaluation and solution key presentation will follow shortly.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 27 of 27
Notes: PROCTORING CUE:
- Collect all answer scripts.
- Count and verify booklet count against attendance sheet (Room R406A).
- Move to evaluation phase using Solution Set PPTX.