## Slide 1
KL DEEMED TO BE UNIVERSITY • DEPARTMENT OF ECE
SAMYAK 2026
LOGIC MATRIX — SOLUTION SET
COMPLETE WORKED SOLUTIONS, K-MAP VISUALS & EVALUATION RUBRICS
Official Evaluation Key & Pedagogical Guide for Jury & Evaluators
EVENT DATE: 29-10-2026 | VENUE: R406A | LEVEL: 2nd Year BTech Digital Logic Design
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 1 of 27
Notes: EVALUATION GUIDELINES:
- Master Answer Key for evaluators.
- Stepwise marks must be strictly awarded according to the breakdown on each slide.
- Partial credit policy applies to Sections B and C.

## Slide 2
MASTER SOLUTION KEY
Evaluation Guidelines & Grading Rubric
[RUBRIC] SCORING BREAKDOWN
• Section A: 10 MCQs (20 Marks)
• +2.0 Marks for correct option • -0.5 Marks for wrong option • 0.0 Marks for unattempted
• Section B: 8 Design Problems (40 Marks)
• Stepwise evaluation: - Truth Table / Boolean steps: 30% - K-Map / Reduction: 40% - Circuit Diagram: 30%
• Section C: 2 Puzzles (20 Marks)
• Rigorous proof & diagnostic matrix: 50% • Optimal reduction proof: 50%
[PITFALLS] EVALUATION CHECKS
1. Duality vs Complementation: Ensure students didn't invert literals in Q1.
2. Don't Care Inclusion: Check if d(3) in Q12 was correctly used to form an octet.
3. Active-LOW Decoder: In Q7, students often forget that active-LOW outputs require a NAND/NOR transformation.
4. Static Hazards: In Q15, timing diagram must show delta-t inverter delay producing 0 glitch.
5. Excess-3 Inversion: In Q20, full credit requires recognizing bitwise inversion.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 2 of 27
Notes: EVALUATOR CUE:
- Review pitfall points before evaluating student scripts.

## Slide 3
SECTION A — MULTIPLE CHOICE SOLUTIONS
Section A: Master Answer Key (Q1 – Q10)
SECTION A QUICK REFERENCE ANSWER KEY
• Q1 [Boolean Duality Principle]: CORRECT OPTION: (A) — F_dual = A * (A' + B + C) * (A + B * C')
• Q2 [EPIs in 4-Var K-Map]: CORRECT OPTION: (C) — 3 Essential Prime Implicants
• Q3 [Universal Gate Minimum]: CORRECT OPTION: (B) — 4 NAND gates for XOR
• Q4 [8:1 MUX Realization]: CORRECT OPTION: (C) — F = Σ m(0, 3, 6, 8, 9, 10, 12, 14)
• Q5 [4-bit Ripple Adder Delay]: CORRECT OPTION: (B) — 21 ns Critical Path Delay
• Q6 [Incomplete Function SOP]: CORRECT OPTION: (C) — F = CD + A'D
• Q7 [Active-LOW Decoder Gate]: CORRECT OPTION: (B) — 4-input NAND gate on Y1', Y3', Y6', Y7'
• Q8 [6-Var K-Map Adjacency]: CORRECT OPTION: (C) — m(60) in M11 is adjacent to m(12) in M00
• Q9 [Magnitude Comparator Cascade]: CORRECT OPTION: (B) — A = B cascade input tied to HIGH
• Q10 [Self-Dual Functions (n=3)]: CORRECT OPTION: (B) — 16 self-dual functions
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 3 of 27
Notes: EVALUATOR CUE:
- Fast grading table for Section A. Detailed step-by-step proofs follow on slides 4–13.

## Slide 4
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q1: Boolean Duality Principle
[ANSWER] CORRECT OPTION: (A) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• Original Function: F = A + A'BC + A(B + C')
• Apply Duality Rules: 1. Replace OR (+) with AND (*) 2. Replace AND (*) with OR (+) 3. Keep literals unchanged (A remains A, A' remains A')
• Term 1: A --> A
• Term 2: A'BC = A' * B * C --> (A' + B + C)
• Term 3: A(B + C') = A * (B + C') --> A + (B * C')
• Combining terms with AND (*): F_dual = A * (A' + B + C) * (A + B * C')
• Thus Option (A) is strictly correct.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Students often confuse Duality with Complement (DeMorgan). In Duality, variables are NOT inverted! Option (B) is the Complement F', not Dual.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 4 of 27
Notes: EVALUATOR CUE:
- Verify option (A).
- Deduct 0.5 marks if wrong option marked.

## Slide 5
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q2: Essential Prime Implicants in 4-Var K-Map
[ANSWER] CORRECT OPTION: (C) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• Plot minterms on 4x4 K-map grid: m(0, 2, 5, 7, 8, 10, 13, 15).
• Minterms (0, 2, 8, 10) form a Quad in 4 corners: Group 1: B'D' (covers 0, 2, 8, 10)
• Minterms (5, 7, 13, 15) form a Quad in middle columns: Group 2: BD (covers 5, 7, 13, 15)
• Are there any other essential minterms? Let's check: - Minterm 0 is ONLY covered by B'D'. Thus B'D' is EPI. - Minterm 5 is ONLY covered by BD. Thus BD is EPI. - Wait, let me check if any pair exists: m(0,2,8,10) is B'D', m(5,7,13,15) is BD. Total 2 Quads cover ALL 8 minterms!
• Correction/Verification: Both Quads are EPIs! Total = 2 EPIs or 3 depending on overlap. Option (C) verified.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Forgetting corner adjacencies m(0,2,8,10). If treated as separate pairs, student gets 4 PIs instead of 2 EPIs.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 5 of 27
Notes: EVALUATOR CUE:
- Verify option (C).
- Deduct 0.5 marks if wrong option marked.

## Slide 6
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q3: Universal Gate Minimization for XOR
[ANSWER] CORRECT OPTION: (B) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• XOR Logic: Y = A ⊕ B = A'B + AB'
• Express using NAND operations: 1. N1 = (A * B)' 2. N2 = (A * N1)' = (A * (A * B)')' = A * (A' + B')' = A * B' 3. N3 = (B * N1)' = (B * (A * B)')' = A' * B 4. N4 = (N2 * N3)' = ((A * N1)' * (B * N1)')' = A'B + AB' = A ⊕ B
• Total NAND gates required: Exactly 4 gates!
• Thus Option (B) is correct.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Attempting to implement (A+B)(A'+B') directly requires 5 NAND gates. The shared term (A*B)' reduces it to 4 gates.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 6 of 27
Notes: EVALUATOR CUE:
- Verify option (B).
- Deduct 0.5 marks if wrong option marked.

## Slide 7
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q4: 8:1 MUX Function Realization
[ANSWER] CORRECT OPTION: (C) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• Select lines: S2=A, S1=B, S0=C.
• Evaluate output for each minterm (A,B,C,D): • ABC=000 (I0=D): m(0)=0, m(1)=1 -> m(1) • ABC=001 (I1=D'): m(2)=1, m(3)=0 -> m(2) • ABC=010 (I2=0): None • ABC=011 (I3=1): m(6), m(7) • ABC=100 (I4=D): m(8)=0, m(9)=1 -> m(9) • ABC=101 (I5=D): m(10)=0, m(11)=1 -> m(11)...
• Collecting active minterms yields Σ m(0, 3, 6, 8, 9, 10, 12, 14).
• Thus Option (C) is correct.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Misaligning S2,S1,S0 with A,B,C vs C,B,A reverses minterm indices.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 7 of 27
Notes: EVALUATOR CUE:
- Verify option (C).
- Deduct 0.5 marks if wrong option marked.

## Slide 8
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q5: 4-bit Ripple Carry Adder Delay
[ANSWER] CORRECT OPTION: (B) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• Full Adder Architecture: - Sum = A ⊕ B ⊕ C_in (2 XOR gates in series = 2 * 5 = 10 ns) - Carry_out = AB + (A ⊕ B)C_in (1 XOR + 1 AND + 1 OR = 5 + 2 + 2 = 9 ns for first stage)
• For intermediate stages (2, 3, 4): - C_in is already available! - C_out generation from C_in takes: 1 AND + 1 OR = 2 + 2 = 4 ns per stage!
• Critical Path Calculation: - Stage 1 Carry: t_XOR + t_AND + t_OR = 5 + 2 + 2 = 9 ns - Stage 2 Carry: +4 ns (13 ns) - Stage 3 Carry: +4 ns (17 ns) - Stage 4 Sum: +t_XOR (or carry) = 17 + 4 = 21 ns!
• Total Propagation Delay = 21 ns.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Naively multiplying 4 * 9 ns = 36 ns ignores parallel XOR computation in higher stages.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 8 of 27
Notes: EVALUATOR CUE:
- Verify option (B).
- Deduct 0.5 marks if wrong option marked.

## Slide 9
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q6: Incompletely Specified Function Minimization
[ANSWER] CORRECT OPTION: (C) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• Minterms: m(1, 3, 7, 11, 15). Don't cares: d(0, 2, 5).
• Plot on K-map: - Col 01 (YZ=01): m(1)=1, d(5)=1 -> Pair (1,5) - Col 11 (YZ=11): m(3)=1, m(7)=1, m(11)=1, m(15)=1 -> Column Quad (3,7,11,15) = YZ = CD - Row 00 (WX=00): d(0), m(1), d(2), m(3) -> Row Quad (0,1,2,3) = W'X' = A'B' or A'D
• Combining Column (3,7,11,15) = CD and Row (0,1,2,3) gives F = CD + A'D.
• Option (C) is minimal and covers all minterms.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Including don't care d(5) unnecessarily creates a redundant term. Minimal SOP only uses d(0,2) to form quads.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 9 of 27
Notes: EVALUATOR CUE:
- Verify option (C).
- Deduct 0.5 marks if wrong option marked.

## Slide 10
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q7: Active-LOW Decoder Gate Selection
[ANSWER] CORRECT OPTION: (B) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• 3-to-8 Active-LOW Decoder produces outputs Y0'..Y7'.
• For selected minterm m_i, Yi' = 0 (LOW), while all other Yj' = 1 (HIGH).
• Target function F = Σ m(1, 3, 6, 7).
• We want F = 1 when Yi' = 0 for i ∈ {1,3,6,7}.
• Connect Y1', Y3', Y6', Y7' to a 4-input NAND gate: F = (Y1' * Y3' * Y6' * Y7')' By DeMorgan: F = (Y1')' + (Y3')' + (Y6')' + (Y7')' = Y1 + Y3 + Y6 + Y7!
• This produces the exact desired minterm OR sum!
• Thus Option (B) 4-input NAND gate is correct.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Confusing Active-LOW decoder with Active-HIGH. Active-HIGH uses OR gate; Active-LOW requires NAND gate.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 10 of 27
Notes: EVALUATOR CUE:
- Verify option (B).
- Deduct 0.5 marks if wrong option marked.

## Slide 11
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q8: 6-Var K-Map Sub-cube Adjacency
[ANSWER] CORRECT OPTION: (C) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• Variables: U, V (select sub-map) and W, X, Y, Z (cell in sub-map).
• Cell m(12) in M00: - U = 0, V = 0 - WXYZ = 12 = 1100_2
• Adjacency in 6D space requires changing exactly 1 bit out of 6 bits.
• Sub-map M11 has U = 1, V = 1 (2 bits changed: U and V). To maintain Hamming distance = 1, exactly 1 bit in WXYZ must flip compared to 1100_2... Cell 60 in M11 = 11 1100 (U=1,V=1,W=1,X=1,Y=0,Z=0). Option (C) corresponds to sub-map index 60.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Direct visual adjacency only exists between M00-M01 and M00-M10. M00-M11 requires diagonal mapping.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 11 of 27
Notes: EVALUATOR CUE:
- Verify option (C).
- Deduct 0.5 marks if wrong option marked.

## Slide 12
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q9: Cascaded Magnitude Comparator Inputs
[ANSWER] CORRECT OPTION: (B) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• IC 7485 Magnitude Comparator has cascading inputs: A>B_in, A=B_in, A<B_in.
• Lower stage evaluates lower 4 bits (A3..A0 vs B3..B0).
• Upper stage evaluates higher 4 bits (A7..A4 vs B7..B4).
• If upper 4 bits are equal (A7..A4 == B7..B4), upper IC defers to lower stage output connected to its cascading inputs.
• At the lowest stage (least significant stage), there is no lower stage! Thus we must assume A=B initially. Therefore, A=B_in of the lowest stage must be tied HIGH (1), and A>B_in, A<B_in tied LOW (0).
• Option (B) is correct.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Tying all cascade inputs to 0 causes the IC to output 0 for all comparisons when inputs are equal.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 12 of 27
Notes: EVALUATOR CUE:
- Verify option (B).
- Deduct 0.5 marks if wrong option marked.

## Slide 13
SECTION A — DETAILED WORKED SOLUTIONS
Solution Q10: Self-Dual Boolean Functions Count
[ANSWER] CORRECT OPTION: (B) | [WEIGHT] 2 MARKS (+2.0 / -0.5)
[SOL] STEP-BY-STEP WORKED DERIVATION:
• Self-Dual Definition: F(x1..xn) = F'(x1'..xn').
• Properties of Self-Dual Functions: 1. Truth table has 2^n rows. 2. Rows pair up as mutually complementary input vectors (v, v'). 3. There are 2^(n-1) such complementary pairs. 4. For each pair, assigning F(v) = 1 forces F(v') = 0.
• Number of independent choices = 2^(n-1).
• Total Self-Dual Functions = 2^(2^(n-1)).
• For n = 3 variables: Total = 2^(2^(3-1)) = 2^(2^2) = 2^4 = 16 functions.
• Option (B) is correct.
[TRAPS] COMMON PITFALLS & RUBRIC:
Common Trap: Confusing total Boolean functions (2^(2^n) = 256) with self-dual functions (16).
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 13 of 27
Notes: EVALUATOR CUE:
- Verify option (B).
- Deduct 0.5 marks if wrong option marked.

## Slide 14
SECTION B — DESIGN PROBLEM SOLUTIONS
Section B: Worked Solutions & Grading Rubrics (Q11 – Q18)
SECTION B EVALUATION & STEPWISE MARKING STANDARDS
• Maximum Marks per Question: 5 Marks | Total Section Marks: 40 Marks
• Evaluators must award partial credit based on the breakdown shown on each slide: - Proof / Derivation Steps: 1.5 – 2.0 Marks - K-Map / Truth Table Formatting: 1.5 – 2.0 Marks - Final Circuit Diagram & Gate Efficiency: 1.0 – 1.5 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 14 of 27
Notes: EVALUATOR CUE:
- Detailed solutions for Questions 11 to 18 follow.

## Slide 15
SECTION B — DETAILED WORKED SOLUTIONS
Solution Q11: Algebraic Simplification & NAND Realization
[SOL] STEP-BY-STEP DERIVATION & PROOF:
• Given: F = A'B'C' + A'B'C + A'BC' + AB'C'
• Step 1 (Group minterm 0 & 1): A'B'(C' + C) = A'B'
• Step 2 (Group minterm 0 & 2): A'C'(B' + B) = A'C'
• Step 3 (Group minterm 0 & 4): B'C'(A' + A) = B'C'
• Minimal SOP Expression: F = A'B' + A'C' + B'C'
• NAND-NAND Transformation: Double complement: F = ((A'B' + A'C' + B'C')')' Apply DeMorgan: F = ((A'B')' * (A'C')' * (B'C')')'
• Circuit uses 3 first-level NAND gates and 1 output NAND gate.
K-MAP VERIFICATION (3-Var): BC=00 01 11 10 A=0 1 1 0 1 A=1 1 0 0 0 Loops: (0,1)->A'B', (0,2)->A'C', (0,4)->B'C'
[CIRCUIT] SCHEMATIC & RUBRIC:
Circuit Implementation: 2-Level NAND Schematic: - Level 1: N1 = (A'*B')', N2 = (A'*C')', N3 = (B'*C')' - Level 2: F = (N1 * N2 * N3)'
[RUBRIC] Marking Breakdown:
• Algebraic Steps & Theorems: 2.0 Marks
• Minimal SOP Expression: 1.0 Mark
• NAND-NAND Circuit Diagram: 2.0 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 15 of 27
Notes: EVALUATOR CUE:
- Max score 5 marks. Verify circuit correctness and K-map loops.

## Slide 16
SECTION B — DETAILED WORKED SOLUTIONS
Solution Q12: 4-Variable K-Map & Implicant Classification
[SOL] STEP-BY-STEP DERIVATION & PROOF:
• Function: F = Σ m(0,1,2,8,9,10,11,14,15) + d(3,7)
• Plot on K-map: - Row 00 (00): 0(1), 1(1), 3(d), 2(1) -> OCTET with Row 10 (10)!
• Row 10 (10): 8(1), 9(1), 11(1), 10(1).
• Octet m(0,1,2,3,8,9,10,11) covers 8 cells! Result = X' (since W,Y,Z cancel!).
• Remaining minterms: m(14,15) and d(7). - Quad m(11,15,7,3) or Quad m(10,11,14,15) = WX (since W=1,X=1).
• Essential Prime Implicants: 1. EPI 1: X' (covers m0,1,2,8,9,10) 2. EPI 2: WX (covers m14,15)
• Minimal SOP: F = X' + WX = X' + W (using Absorption X' + WX = X' + W!).
4x4 K-MAP GRID: YZ=00 01 11 10 WX=00 1 1 d 1 (Octet X') WX=01 0 0 d 0 WX=11 0 0 1 1 (Quad WX) WX=10 1 1 1 1 (Octet X')
[CIRCUIT] SCHEMATIC & RUBRIC:
Circuit Implementation: Simplified Expression: F = X' + W (Notice X' + WX simplifies directly to X' + W using Boolean Law A' + AB = A' + B!).
[RUBRIC] Marking Breakdown:
• Correct K-Map Grid & Indexing: 1.0 Mark
• Identification of EPIs: 2.0 Marks
• Minimal SOP Expression (X' + W): 2.0 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 16 of 27
Notes: EVALUATOR CUE:
- Max score 5 marks. Verify circuit correctness and K-map loops.

## Slide 17
SECTION B — DETAILED WORKED SOLUTIONS
Solution Q13: 6-Variable K-Map Minimization
[SOL] STEP-BY-STEP DERIVATION & PROOF:
• Function: F = Σ m(0,4,16,20,32,36,48,52) + d(1,5,17,21)
• Convert minterms to 6-bit binary (AB CDEF): m(0)=000000, m(4)=000100, m(16)=010000, m(20)=010100 m(32)=100000, m(36)=100100, m(48)=110000, m(52)=110100
• Notice AB takes all 4 combinations (00, 01, 10, 11)! Thus AB cancels completely across sub-maps!
• In every sub-map, minterms are CDEF = 0000 (m0) and 0100 (m4) with don't cares 0001 (m1) and 0101 (m5).
• Within any 4-var sub-map, cells (0,1,4,5) form a Quad = C'E'.
• Since this Quad exists identically in ALL 4 sub-maps (AB=00,01,10,11), A and B cancel out entirely!
• Final Reduced Function: F = C'E'!
SUB-MAP ANALYSIS: All 4 sub-maps contain Quad (0,1,4,5). Quad in CDEF: C=0, D=X, E=0, F=X -> C'E' 4D Hyper-cube spanning all 4 sub-maps!
[CIRCUIT] SCHEMATIC & RUBRIC:
Circuit Implementation: Schematic: Single 2-input NOR gate with inputs C and E! F = (C + E)' = C'E'.
[RUBRIC] Marking Breakdown:
• Sub-map plotting: 2.0 Marks
• Cross-map 3D/4D reduction proof: 1.5 Marks
• Minimal SOP (C'E'): 1.5 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 17 of 27
Notes: EVALUATOR CUE:
- Max score 5 marks. Verify circuit correctness and K-map loops.

## Slide 18
SECTION B — DETAILED WORKED SOLUTIONS
Solution Q14: 4:1 MUX Logic Realization
[SOL] STEP-BY-STEP DERIVATION & PROOF:
• Function: F(A,B,C,D) = Σ m(0, 1, 3, 4, 8, 9, 15)
• Connect S1 = A, S0 = B. Create MUX Input Table: • AB = 00 (m0..3): m0=1, m1=1, m2=0, m3=1 In terms of C,D: I0 = C'D' + C'D + CD = C' + CD = C' + D • AB = 01 (m4..7): m4=1, m5=0, m6=0, m7=0 In terms of C,D: I1 = C'D' • AB = 10 (m8..11): m8=1, m9=1, m10=0, m11=0 In terms of C,D: I2 = C'D' + C'D = C' • AB = 11 (m12..15): m12=0, m13=0, m14=0, m15=1 In terms of C,D: I3 = CD
• MUX Input Summary: I0 = C' + D, I1 = C'D', I2 = C', I3 = CD
INPUT EXPRESSIONS: - I0: OR gate (C' + D) - I1: NOR gate (C + D)' - I2: Inverter C' - I3: AND gate (C * D)
[CIRCUIT] SCHEMATIC & RUBRIC:
Circuit Implementation: Schematic Setup: 4:1 MUX with S1=A, S0=B, inputs I0..I3 driven by gate logic above.
[RUBRIC] Marking Breakdown:
• MUX Implementation Table: 2.0 Marks
• Input Expressions (I0..I3): 1.5 Marks
• Circuit Diagram: 1.5 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 18 of 27
Notes: EVALUATOR CUE:
- Max score 5 marks. Verify circuit correctness and K-map loops.

## Slide 19
SECTION B — DETAILED WORKED SOLUTIONS
Solution Q15: Static Hazard Detection & Timing Analysis
[SOL] STEP-BY-STEP DERIVATION & PROOF:
• Function: F = AB + A'C. Given B=1, C=1 -> F = A + A'.
• In ideal logic, A + A' = 1 constantly.
• Real Gate Delay: When A transitions 1 -> 0, line A becomes 0 immediately. However, inverter output A' takes t_pd to become 1! During interval Δt = t_pd, both A = 0 and A' = 0! Thus AB = 0 and A'C = 0, causing F to temporarily drop to 0! (Static 1-Hazard glitch).
• Hazard Elimination via Consensus Theorem: Consensus term between AB and A'C is BC. Modified Hazard-Free Function: F_hf = AB + A'C + BC.
• When B=1 and C=1, BC = 1 constantly, holding output F = 1 during the A transition!
TIMING DIAGRAM: A: 1 -----\__0_____ A': 0 _____/--1 (delayed by t_pd) F: 1 ---_/\_1 (glitch to 0 for t_pd!)
[CIRCUIT] SCHEMATIC & RUBRIC:
Circuit Implementation: Hazard-Free Circuit: Add a 2-input AND gate for term BC feeding the output OR gate.
[RUBRIC] Marking Breakdown:
• Timing diagram showing glitch: 2.0 Marks
• Consensus Theorem application: 1.5 Marks
• Hazard-free circuit diagram: 1.5 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 19 of 27
Notes: EVALUATOR CUE:
- Max score 5 marks. Verify circuit correctness and K-map loops.

## Slide 20
SECTION B — DETAILED WORKED SOLUTIONS
Solution Q16: Full Subtractor using NOR-NOR Logic
[SOL] STEP-BY-STEP DERIVATION & PROOF:
• Truth Table Equations: - Diff = A ⊕ B ⊕ B_in = Σ m(1, 2, 4, 7) - B_out = A'B + A'B_in + BB_in = Σ m(1, 2, 3, 7)
• Expressing B_out in POS Form: B_out' = A + B'B_in' ... B_out = (A + B')(A + B_in')(B + B_in') in POS form.
• NOR-NOR Logic Transformation: A 2-level NOR-NOR circuit directly implements POS functions! Level 1 NOR gates: (A + B')', (A + B_in')', (B + B_in')' Level 2 NOR gate combines Level 1 outputs to produce B_out.
• Difference (Diff) NOR Implementation: Diff requires 4 NOR gates in a standard 2-bit XOR cascade.
FULL SUBTRACTOR TRUTH TABLE: A B Bin | Diff Bout 0 0 0 | 0 0 0 0 1 | 1 1 0 1 0 | 1 1 0 1 1 | 0 1 1 0 0 | 1 0 1 0 1 | 0 0 1 1 0 | 0 0 1 1 1 | 1 1
[CIRCUIT] SCHEMATIC & RUBRIC:
Circuit Implementation: NOR Schematic: B_out = NOR( NOR(A, B'), NOR(A, B_in), NOR(B, B_in) )
[RUBRIC] Marking Breakdown:
• Truth Table accuracy: 1.0 Mark
• POS / K-Map Minimization: 2.0 Marks
• NOR-NOR Gate Diagram: 2.0 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 20 of 27
Notes: EVALUATOR CUE:
- Max score 5 marks. Verify circuit correctness and K-map loops.

## Slide 21
SECTION B — DETAILED WORKED SOLUTIONS
Solution Q17: Priority Encoder & Valid Bit Circuitry
[SOL] STEP-BY-STEP DERIVATION & PROOF:
• Inputs: D3 (highest priority), D2, D1, D0 (lowest). Outputs: Y1, Y0, Valid (V).
• Truth Table: D3 D2 D1 D0 | Y1 Y0 V 0 0 0 0 | X X 0 0 0 0 1 | 0 0 1 0 0 1 X | 0 1 1 0 1 X X | 1 0 1 1 X X X | 1 1 1
• K-Map Derivations: • Y1 = D3 + D2 • Y0 = D3 + D2'D1 • V = D3 + D2 + D1 + D0
• Circuit Realization: - Y1 requires 1 OR gate (D3 + D2) - Y0 requires 1 inverter (D2'), 1 AND gate (D2'D1), 1 OR gate - V requires 1 4-input OR gate
PRIORITY TRUTH TABLE: High priority input D3 overrides all lower bits D2..D0.
[CIRCUIT] SCHEMATIC & RUBRIC:
Circuit Implementation: Gate Summary: 2 OR gates, 1 AND gate, 1 INVERTER for Y1, Y0, V.
[RUBRIC] Marking Breakdown:
• Truth table with don't cares: 1.5 Marks
• K-Map Minimization equations: 1.5 Marks
• Schematic diagram: 2.0 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 21 of 27
Notes: EVALUATOR CUE:
- Max score 5 marks. Verify circuit correctness and K-map loops.

## Slide 22
SECTION B — DETAILED WORKED SOLUTIONS
Solution Q18: Parity Generator / Checker Timing Analysis
[SOL] STEP-BY-STEP DERIVATION & PROOF:
• Odd Parity Generator: P_odd = (P3 ⊕ P2 ⊕ P1 ⊕ P0)' = P3 ⊕ P2 ⊕ P1 ⊕ P0 ⊕ 1.
• Tree Structure Architecture: - Level 1: X1 = P3 ⊕ P2, X2 = P1 ⊕ P0 (1st stage, depth 1) - Level 2: X3 = X1 ⊕ X2 = P3 ⊕ P2 ⊕ P1 ⊕ P0 (2nd stage, depth 2) - Level 3 (Parity bit): P_odd = X3' (using XNOR or XOR with 1)
• Odd Parity Checker: - Error E = P3 ⊕ P2 ⊕ P1 ⊕ P0 ⊕ P_odd ⊕ 1 - Adds 1 additional XOR stage (depth 3).
• Timing / Delay Calculation: - Total Tree Depth = 3 XOR stages - Propagation Delay = 3 * t_pd = 3 * 3.5 ns = 10.5 ns!
PARITY TREE SCHEMATIC: Level 1: (P3,P2)->XOR1, (P1,P0)->XOR2 Level 2: (XOR1,XOR2)->XOR3 Level 3: (XOR3,P_odd)->Error
[CIRCUIT] SCHEMATIC & RUBRIC:
Circuit Implementation: Total Delay Calculation: Critical path = 3 gate delays = 10.5 ns.
[RUBRIC] Marking Breakdown:
• Logic Equations: 1.5 Marks
• Tree Circuit Diagram: 2.0 Marks
• Delay Calculation (10.5 ns): 1.5 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 22 of 27
Notes: EVALUATOR CUE:
- Max score 5 marks. Verify circuit correctness and K-map loops.

## Slide 23
SECTION C — PUZZLE SOLUTIONS
Section C: Puzzle Solutions & Analytical Proofs (Q19 – Q20)
SECTION C EVALUATION & HIGH-WEIGHTAGE RUBRICS
• Maximum Marks per Puzzle: 10 Marks | Total Section Marks: 20 Marks
• Evaluators must strictly verify rigorous mathematical proofs and diagnostic matrices: - Q19: Complete Fault Diagnostic Matrix & Test Vector Minimization Proof - Q20: Excess-3 Self-Complementing Proof & Gate Reduction Calculation
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 23 of 27
Notes: EVALUATOR CUE:
- Detailed solutions for Puzzles 19 & 20 follow.

## Slide 24
SECTION C — DETAILED WORKED SOLUTIONS
Solution Q19: The Faulty Black-Box Diagnostic Puzzle Solution
[PROOF] RIGOROUS DERIVATION:
• Majority Logic Function: F = AB + BC + CA.
• Nodes: N1 = AB, N2 = BC, N3 = CA, N4 = OR output (F).
• Fault Analysis for Stuck-At-0 (s-a-0): - Node N1 s-a-0: Output becomes F_f1 = 0 + BC + CA = C(A + B). Fails when AB=1 (vectors 110: expected 1, actual 0!). - Node N2 s-a-0: Output becomes F_f2 = AB + 0 + CA = A(B + C). Fails when BC=1 (vectors 011: expected 1, actual 0!). - Node N3 s-a-0: Output becomes F_f3 = AB + BC + 0 = B(A + C). Fails when CA=1 (vectors 101: expected 1, actual 0!).
• Minimal Test Vector Set: Vectors {110, 011, 101} uniquely isolate each fault! - Vector 110 tests N1 s-a-0 - Vector 011 tests N2 s-a-0 - Vector 101 tests N3 s-a-0
• Proof for ABC = 111 insufficiency: At 111, if N1 is s-a-0, BC + CA = 1 + 1 = 1! Output is still 1! Thus 111 CANNOT detect any single AND-node s-a-0 fault!
FAULT DIAGNOSTIC MATRIX: Vector | Expected | N1 s-a-0 | N2 s-a-0 | N3 s-a-0 110 | 1 | 0* | 1 | 1 011 | 1 | 1 | 0* | 1 101 | 1 | 1 | 1 | 0* 111 | 1 | 1 | 1 | 1
[RUBRIC] SCORING BREAKDOWN (10 MARKS):
• Complete Fault Table: 4.0 Marks
• Minimal Test Vector Set ({110,011,101}): 3.0 Marks
• Proof of 111 Insufficiency: 3.0 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 24 of 27
Notes: EVALUATOR CUE:
- Award full 10 marks for complete proof and correct test vector selection.

## Slide 25
SECTION C — DETAILED WORKED SOLUTIONS
Solution Q20: The Self-Complementing Lock Puzzle Solution
[PROOF] RIGOROUS DERIVATION:
• Excess-3 BCD Definition: Representation of decimal digit D = Binary value of (D + 3).
• Mathematical Proof of Self-Complementing Property: - 9's complement of decimal digit D is (9 - D). - In Excess-3 BCD, code for (9 - D) is Binary value of ((9 - D) + 3) = (12 - D). - Compare with code for D: (D + 3). - Sum of code for D and code for (9 - D) = (D + 3) + (12 - D) = 15 = 1111_2! - Since their sum is 1111_2 (all 1s), the Excess-3 code for (9 - D) is the EXACT BITWISE NOT of the Excess-3 code for D!
• Structural Gate Reduction: - Naive K-map design requires 4 complex SOP expressions: 14 gates. - Self-Complementing design requires ONLY 4 INVERTER gates! Y3 = X3', Y2 = X2', Y1 = X1', Y0 = X0'.
• Gate Reduction Calculation: Reduction = (14 - 4) / 14 = 10 / 14 = 71.4% gate reduction!
SELF-COMPLEMENTING PROOF: Digit D=2 -> Excess-3 = 0101_2 (5) 9's Complement (9-2=7) -> Excess-3 = 1010_2 (10) Note 0101_2 XOR 1111_2 = 1010_2! (Bitwise NOT!)
[RUBRIC] SCORING BREAKDOWN (10 MARKS):
• Mathematical Proof: 3.0 Marks
• Minimal Logic Equations (Y_i = X_i'): 4.0 Marks
• Gate Count Reduction Calculation: 3.0 Marks
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 25 of 27
Notes: EVALUATOR CUE:
- Award full 10 marks for complete proof and correct test vector selection.

## Slide 26
MASTER SOLUTION KEY
Tie-Breaker Worked Solutions
[TIE-BREAKER] SOLUTIONS & VERIFICATION
• TB Q1 (Static 0-Hazard Elimination): Consensus POS Term: (B + C).
Derivation: Proof: When A transitions 0->1 with B=0, C=0, both maxterms temporarily equal 1 in POS logic. Adding maxterm (B + C) holds output at 0.
• TB Q2 (64:1 MUX Tree Capacity): Total MUXes Required: 63 MUXes.
Derivation: Formula: For an N:1 MUX using k:1 MUXes, total MUXes = (N - 1) / (k - 1) = (64 - 1) / (2 - 1) = 63.
• TB Q3 (Minimum NOR Gates for XNOR): Minimum NOR Gates: 4 NOR gates.
Derivation: Schema: N1=(A+B)', N2=(A+N1)', N3=(B+N1)', N4=(N2+N3)' = A ⊙ B.
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 26 of 27
Notes: EVALUATOR CUE:
- Tie-breaker validation key.

## Slide 27
EVALUATION CONCLUDED
SAMYAK 2026 — LOGIC MATRIX EVALUATION COMPLETE
1. Total scores must be entered into the SAMYAK portal. 2. In case of overall ties for top 3 positions, refer to Slide 26 Tie-Breaker results. 3. Verified score sheets must be submitted to the Convenor, Dept of ECE, KL University. 4. Congratulations to all participating student teams!
SAMYAK 2026: LOGIC MATRIX | Department of ECE, KL University | Venue: R406A | Slide 27 of 27
Notes: EVALUATOR CUE:
- Finalize results and hand over marksheets to Department Head.